## Slide 1
VARIABLE VOLTAGE
LINEAR POWER SUPPLY
By Team Wave-Formers
EN2091 - Laboratory Practice and Projects

## Slide 2
INTRODUCTION
This project is to design and implement a variable voltage linear power supply. The power supply is designed to provide a regulated DC output voltage ranging from 2V to 20V, with a maximum current output of 2.5A.

## Slide 3
COMPONENTS
Transformer | 24 V(rms) , 5A
Bridge Rectifier | BR 5010
Voltage Regulator | LD1085CT
Transistors | TIP 142 (Darlington), 2N3904
Zener Diodes | 24V (1W)
Potentiometers | 10K ,20K
Capacitors | 2200uF , 10uF , 22nF
Resistors | -
Digital Multimeter | 

## Slide 4
SPICE MODEL

## Slide 5
SIMULATION (LT-SPICE)

## Slide 6
  Component: BR5010 Bridge Rectifier
  Max Reverse Voltage (PIV): 1000V
  Max Forward Current: 50A
  Forward Voltage Drop: ~1V per diode (2V total for a bridge rectifier)
  Input: 24V AC from transformer
  Output: 34V peak rectified DC voltage
https://www.alldatasheet.com/datasheet-pdf/download/58688/DCCOM/BR5010.html
VOLTAGE RECTIFICATION
DATASHEET:
  Component: 24V 5A Transformer
  Input Voltage: 230V AC, 50Hz
  Output Voltage: 24V AC
  Current Rating: 5A (max)

## Slide 7
  NPN Darlington Transistor (TIP142): The passing element for the regulation circuit.
VOLTAGE REGULATING & CURRENT LIMITING CIRCUIT
  24V Zener Diode: Sets the base voltage of the TIP142, allowing it to be used for the initial voltage regulation.
  Max Ic = 2.5A (max current supply)
  Max Power Dissipation
= 2.5A x 9.6 V
= 24 W
max Power Dissipation = 125 W
  TIP142 :
max current: 10 A
  Vce = (34 - 25.4) V = 9.6 V

## Slide 8
I max =
0.672 V
0.26R
VOLTAGE REGULATING & CURRENT LIMITING CIRCUIT
  NPN Transistor (2N3904): The passing element for the current limiter circuit.
  Current Limitation = 2.58 A (Calculated)
  Equivalent Resistance = 0.26 R (Measured)
  Operating V be = 0.672 V (Measured)
  For Short Circuit Protection,
  3 A Fuse used

## Slide 9
This IC is used as a adjustable voltage regulator .The voltage of the output pin is varied by changing the voltage at the adjustable pin using a 10K potentiometer.
LT1085 Voltage Regulator IC: Provides further ripple reduction and adjustable output voltage. (I max = 3A)
VOLTAGE VARIATION

## Slide 10
NOISE
Without probe connected
With probe connected

## Slide 11
SMOOTHING EFFECT AND RIPPLE REJECTION
  Required smoothing capacitor value - 42.5mF (Calculated)
  Used smoothing capacitor value - 4.4mF(Tested)
  LT1085 has high ripple rejection ratio around 70dB at 100 Hz.

## Slide 12
SCHEMATIC

## Slide 13
PCB DESIGN
  2 layer pcb - 1oz copper
  Designed using Altium Designer and manufactured by JLCPCB
  Dimensions - 86.4mm x 64.0mm

## Slide 14
Dimensions (LxWxH) | 20 cmx 20 cm x 10cm
Material | Zn coated steel (0.8mm)
Material Weight | ~500 g
Total Weight | ~3.2 Kg
ENCLOSURE DESIGN
  Designed using SOLIDWORKS (sheet-metal design)

## Slide 15
TEAM MEMBERS & TASK ALLOCATION
220046R ASURAMUNI S. Y.
220280D JAYAWARDENA H.D.S.S.
220429U NIMANTHA K.L.W.O.
220692R WERAGODA W.A.A.P.
  Enclosure Design
  Circuit Design & Calculations
  PCB Design
  Component selection
  Component selection
  Product Assembly
  PCB Design
  Testing & Debugging
  Product Assembly
  Testing & Debugging
  Documentation
  Circuit Design

## Slide 16
THANK YOU